## Slide 1: CS597: Concurrency and Algorithms
FFT Compute Shader
Francis Joseph Serina

## Slide 2: Objectives
Port Parallel FFT to GPU

## Slide 3: Approach 1
Port C++ to DirectCompute with a similar approach
CPU Approach
  Slice image horizontally for worker threads
  Each worker performs FFT by row on their assigned rows
  Main thread aggregates transformed rows and repeats by column
GPU Approach
  Pass whole image to the GPU
  Each thread is assigned 1 row to transform
  When all rows are done, repeat process by column

## Slide 4: Assessment of Approach 1
Advantages
  Easy to implement
Disadvantages
  There are pixels that are ‘waiting’

## Slide 5: Approach 2
1 Thread Per Pixel
Inspiration: Bitonic Sorting
Advantage
  No idle pixels
  No loops in GPU, all kernels have a fixed running time
Disadvantage
  Completely different implementation
  Butterfly network stages are dispatched/blocked by the CPU

## Slide 6: Results
Dimensions | Total Pixels | By CPU Threads | By Compute Shader
2048x1024 | 2,097,152 |  | 
4096x2048 | 8,388,608 | ~180s | 2ms
Results may be skewed because these are 2 different languages (systems)
CPU: Intel Core i7-7700, 8 Cores
GPU: Nvidia GTX 1070 Ti
The following are ignored
  Loading image to memory
  Saving image

## Slide 7: Techniques
Treat Compute Shaders as State Machines
Have a class represent the Compute Shader
  Internally handle Double Buffer
  1 Method per Kernel
Extra Care when declaring data types
  All Data Types should match EXACTLY in the CPU and the GPU
  Uint division is different from int division
  Conversion does not occur when transferring data

## Slide 8: Sample Output